## Slide 1: BoonDocks LED Controller
Operating description
Screen Layouts

## Slide 2
CTL X Name
Username
Username
Username
Username
User Name
100%
50%
25%
0%
Dimmer Touch Cycle
Default “on” 100%
Bulb “ON” / “OFF” State
Haptic response on touch
Click – ringer “ON”
Vibrate – ringer “OFF”
Haptic response on touch
Click – ringer “ON”
Vibrate – ringer “OFF”
Operating Screens
Screen used for
RGBW or RBG + 1
Screen used for
4 independent
channels
Each controller will have its own screen
Icon Operation
Color wheel operation
Bluetooth to pico RGB
LED values as finger
Moves through wheel
Haptic response on releas
Click – ringer “ON”
Vibrate – ringer “OFF”

## Slide 3
RGBW Name
RGB Name
Chan4 Name
Chan1 Name
Chan2 Name
Chan3 Name
Chan4 Name
RGB Name
Chan4 Name
Application Operating Page Sequences
LED Controller 1
LED Controller 2
LED Controller 3
LED Controller 4
Scene
Scene
Scene
Scene
Splash Screen
On App Open
Not in screen rotation in operation
Swipe in app left or right to advance to next screen page rotating back from CTL 4 to Scene page on left swipe. Visa-versa, a right swipe will go from the Scene page to the CTL 4 page.
BoonDocks
LED Controls
Scene MGMT

## Slide 4
Scene Selection and Screen Saving
Scene
Scene
Scene
Scene
Scene 2
User Name
Save Scene
Scene
Scene
Scene
Scene
Scene
Scene
Scene
Scene
Momentary touch < 5 seconds
The scene box turns green to indicate it is selected and will remain selected.
Longer touch > 5 seconds
The scene naming and save screen is presented.
Haptic response as scene is touched
Highlight text box green
Click – ringer “ON”
Vibrate – ringer “OFF”
Scene 1
User Name
Save Scene
This is a static field for S 1/2/3/4
User name input from keyboard
Save to pico & return to Scene page green highlighted
Scene
Scene
Scene
Scene
Touching this icon takes you to setup page

## Slide 5
BoonDocks
LED Controls
Splash Screen and Bluetooth Conection
App start Splash Screen
Cannot swipe out
BoonDocks
LED Controls
Prompt user to connect to system in the native BT environment
App starts, established BT connection, waiting tbd seconds for success before prompting user with the native BT connection screen on the phone.
To be determined as needed by Android operating system environment
Bluetooth connected
Can swipe out to operating screens
System Configuration
*****NOTE******
After BT connection, the APP will upload the system’s JSON stored configuration. This is such that a another/second user to the system will not need to reprogram all the board configs, names, scenes etc.

## Slide 6
Setup Configuration Screen
LED CTL 1
LED CTL 2
LED CTL 3
LED CTL 4
LED CTL X
RGBW
RGB + 1
4 Channel
Return to Scene page
LED CTL X RGBW
Username
Save CTL X
LED CTL X RGB +1
RGB Name
Save CTL X
+1 Name
CH 1 Name
CH 3 Name
CH 2 Name
CH 4 Name
The touch of a box on the Setup Splash takes user to the board config screen. The user selects 1 of 3 configs which then takes the user to the Board naming screen. After the name is saved in the naming page, the system will return to the Setup Splash; and, the text box will be highlighted to show it is setup.
Setup splash
Board Config
Return to Setup Splash page
Save CTL X